## Slide 1: Data and Computer Communications
Ninth Edition
by William Stallings
Chapter 5 – Signal Encoding Techniques

## Slide 2
Major 4 Encoding Methods
Digital Data
To
Digital Signal
Digital Data
To
Analog Signal
Analog Data
To
Digital Signal
Analog Data
To
Analog Signal

## Slide 3: Digital to Digital Conversion
Converting binary 0’s and 1’s into a sequence of voltage pulses that can propagate over a wire.

## Slide 4: Line Coding and Decoding

## Slide 5: Line Coding

## Slide 6: Line Coding
unipolar – all signal elements have the same sign
polar – one logic state represented by positive voltage and the other by negative voltage
Bipolar – three voltage levels: positive, zero, and negative

## Slide 7: DC components
Some coding schemes have a residual DC [Direct-Current] that has a zero frequency. The positive and negative voltages do not cancel each other.
Not Desirable
  This extra energy on the line is useless and will not pass properly through Transformers! Bad!
    직류성분을 다룰 수 없는 매체는 통과 불가능
  Capacitive Coupling

## Slide 8: DC components

## Slide 9: Synchronization
To interpret the received signal correctly, the bit interval of the receiver should be exactly same or within certain limit of that of the transmitter.
Any mismatch between the two may lead wrong interpretation of the received signal.

## Slide 10: Unipolar
the polarity is assigned to ‘1’ bit, while the ‘0’ bit is represented by zero voltage.
  use one voltage level

## Slide 11: Unipolar
Unipolar requires DC component
  Average amplitude is non-zero
  Not all mediums can handle a DC component
Unipolar requires synchronization
  No way receiver can determine beginning or end
  Problem with a long, uninterrupted series of 1’s or 0’s
Solution to synchronization problem
  Use a separate parallel line to carry clock pulse
  Doubling # lines expensive

## Slide 12: Polar
Two voltage levels
  0 - positive & 1 – negative
  or vice versa
Average amplitude is 0
DC component not needed

## Slide 13: Return to Zero (RZ)
Return to Zero (RZ) uses three values: positive, negative and zero. In RZ, the signal changes not between bits but during (middle of) each bit.
A 1 bit is represented by positive-to-zero and a 0 bit by negative-to-zero.
The main disadvantage of RZ is that it requires two signal changes to encode one bit and therefore occupies more bandwidth.

## Slide 14: Return to Zero (RZ)
3 levels of amplitude – 3 voltage levels
A signal change with every bit to assure synchronization

## Slide 15: Manchester Encoding
transition in middle of each bit period
midbit transition serves as synchronization and data (bit representation)
low to high transition : 1
high to low transition : 0
used by IEEE 802.3 (LAN)

## Slide 16: Manchester Encoding
Two levels of amplitude
Same synchronization as RZ
Example

## Slide 17: Bipolar
three voltage levels: positive, zero, and negative.
The zero level is used to represent binary 0.
The 1s are represented by alternating positive and negative voltages (even if the 1 bits are not consecutive).
A common bipolar encoding scheme is called Alternate Mark Inversion (AMI). The word mark comes from telegraphy and it means 1.

## Slide 18: Bipolar AMI Encoding

## Slide 19
Major 4 Encoding Methods
Digital Data
To
Digital Signal
Digital Data
To
Analog Signal
Analog Data
To
Digital Signal
Analog Data
To
Analog Signal

## Slide 20: Digital Data, Analog Signal

## Slide 21: Digital Data, Analog Signal
반송파 신호 (Carrier)
  반송파 신호
    정보를 실어 보내는 사인(sine)파 또는 펄스(pulse)파
    아날로그 전송에서 정보 신호의 기반이 되는 고주파 신호
  반송파 신호의 특성
    진폭 (A)
    주파수 (f)
    위상 ()
  변조
    반송파 신호의 특성 중 한가지 이상을 변화시키는 방식

## Slide 22: Digital Data, Analog Signal

## Slide 23: Modulation Techniques

## Slide 24: Amplitude Shift Keying
  진폭 차이
  주파수와 위상은 변하지 않음

## Slide 25: Amplitude Shift Keying
encode 0/1 by different carrier amplitudes
  usually have one amplitude zero
  presence and absence of carrier

## Slide 26: Binary Frequency Shift Keying
two binary values represented by two different frequencies (near and on both sides of a central carrier frequency fc)

## Slide 27: FSK
Carrier 2
Data
signal
Carrier 1
vd(t)
v1(t), f1
v2(t), f2
vFSK(t)

## Slide 28: Phase Shift Keying
위상(Phase)
  진동이나 파동과 같이 주기적으로 반복 되는 현상에 대해 어떤 시각 또는 어떤 지점에서의 변화의 상태
  시각 0시에 대한 파형의 상대적인 위치

## Slide 29: Phase Shift Keying
phase of carrier signal is shifted to represent data
Binary PSK (BPSK)
  two phases (spaced at 180) represent two binary digits

## Slide 30: Quadrature Amplitude Modulation (QAM)
combination of ASK and PSK
improved data rate for given bandwidth
  increased potential error rate

## Slide 31: QAM Variants
8-QAM
  ASK with 2 levels
  PSK with 4 levels
Modulation of PSK
Modulation of ASK
QAM

## Slide 32
M=256
M=128
M=64
M=32
M=16
M=4
+

## Slide 33
Major 4 Encoding Methods
Digital Data
To
Digital Signal
Digital Data
To
Analog Signal
Analog Data
To
Digital Signal
Analog Data
To
Analog Signal

## Slide 34: Analog Data, Digital Signal
digitization is conversion of analog data into digital data which can then:
  be transmitted using Digital Data To Digital Signal encoding techniques
analog to digital conversion done using a codec
  pulse code modulation (PCM)
  delta modulation (DM)
  …

## Slide 35: Digitizing Analog Data

## Slide 36: Pulse Code Modulation (PCM)
Step1: Sampling (표본화)
  Sample analog data at regular intervals
  Pulse Amplitude Modulation (PAM)
Step2: Quantization (양자화)
  Quantize PAM value
Step3: Binary Encoding (부호화)
  Translate each value into n bit binary equivalent

## Slide 38: Pulse Code Modulation (PCM)
sampling theorem:
  “If a signal is sampled at regular intervals at a rate higher than twice the highest signal frequency, the samples contain all information in original signal”
  eg. 4000Hz voice data, requires 8000 sample per second

## Slide 39: PCM 절차
양자화 비트 수 (Quantization Bit Depth): n
  샘플된 값을 몇 개의 비트로 표현하는가를 나타냄
  비트 수가 클수록 더 세밀하게 표현 가능
양자화 레벨 수 (Quantization Level Number): L
  L = 2n
최대 입력 범위 (Full Scale Range) / 동적 범위 (Dynamic Range): D
  입력된 아날로그 신호 값의 최대 동적 범위
양자화 단위 (Quantization Step Size): δ
  δ = D / L = D / 2n

## Slide 40: PCM Example

## Slide 41: PCM Example

## Slide 42: PCM Example

## Slide 43: PCM Example
Bit Depth | Quality Level | Amplitude Values | Dynamic Range
8 bit | Telephony | 256 | 48.16dB
16 bit | Audio CD | 65,536 | 96.33dB
24 bit | Audio DVD | 16,777,216 | 144.49dB
32 bit | Best | 4,294,967,296 | 192.66dB
* MP3: 16 bit PCM
동적 범위 | - 일반적으로, 기기를 원하는 상태로 사용 가능한 동작범위 - 입력에서 주어질 수 있는 가장 큰 신호와 가장 작은 신호의 차이
마이크로폰 | 가장 작은 소리에서 가장 큰 소리까지 수음 범위 (약 140dB)
인간 청각 | 가장 작은 소리에서 가장 큰 소리까지 가청 범위 (약 120dB)
스피커 | 가장 작은 소리에서 가장 큰 소리까지 재생 범위

## Slide 44
Major 4 Encoding Methods
Digital Data
To
Digital Signal
Digital Data
To
Analog Signal
Analog Data
To
Digital Signal
Analog Data
To
Analog Signal

## Slide 45: Analog Data, Analog Signals

## Slide 46: Analog Data, Analog Signals
modulate carrier frequency with analog data
why modulate analog signals?
  higher frequency can give more efficient transmission
  permits frequency division multiplexing
types of modulation:
  Amplitude modulation
  Angle modulation
    Frequency
    Phase

## Slide 47: Amplitude Modulation
The amplitude of high-carrier signal is varied according to the instantaneous amplitude of the modulating message signal m(t).

## Slide 48: Amplitude Modulation

## Slide 49: Amplitude Modulation

## Slide 50: Amplitude Modulation
Diagram
Modulating
Signal m(t)
DC Ac
cos2πfct
Ac + m(t)
s(t)

## Slide 51: Amplitude Modulation
m(t)
Ac + m(t)
(Ac + m(t)) • cos2πfct

## Slide 52: AM Demodulation

## Slide 53: Angle Modulation
Angle modulation
Phase Modulation(PM)
    Phase is proportional to modulating signal m(t)
      np = phase modulation index in radians/volt
Frequency Modulation(FM)
    Derivative of the phase is proportional to modulating signal m(t)
      nf = frequency modulation index in radians/volt

## Slide 54: Angular Velocity
Since phase changes nonuniformly vs. time, we can define a rate of change
This is what we know as frequency

## Slide 55: Example
Instantaneous frequency?
Solution

## Slide 56: Phase Modulation(PM)
In PM, carrier angle changes linearly with the message
Instantaneous frequency

## Slide 57: Frequency Modulation(FM)
In FM, it is the instantaneous frequency that varies linearly with message amplitude.
Modulated Signal
Instantaneous frequency

## Slide 58: Illustrating FM & PM

## Slide 59: FM Demodulation
Remember that message in an FM signal is in the instantaneous frequency or equivalently derivative of carrier angle
Do envelope detection on s’(t)

## Slide 60: FM Demodulation
Waveform of the output signal (similar to AM demodulation)